## Slide 1
Towards Top-Down Just Noticeable Difference Estimation of Natural Images
IEEE Transactions on Image Processing, 2022
Qiuping Jiang1, Zhentao Liu1, Shiqi Wang2, Feng Shao1, Weisi Lin3
1. Ningbo University,
2. City University of Hong Kong,
3. Nanyang Technological University

## Slide 2
OUTLINE
Introduction
  Mathematical definition of JND
  Design philosophy comparison
KLTJND: Top-Down JND model based on KLT
  Motivation to apply KLT
  JND estimation based on CPL Image Prediction
Experimental Results
  Performance comparison on direct JND prediction
  JND-guided noise injection
  JND-guided image compression
Conclusion

## Slide 3
Introduction
Mathematical definition of JND
JND map represents the maximum tolerant intensity value variation of each pixel in the original image. JND model try to estimate the maximum change magnitude of each pixel that typical HVS cannot perceive.

## Slide 4
Introduction
Design philosophy comparison
Traditional: Bottom-Up
Model contributing factors
Integrate masking effects
JND map
KLTJND: Top-Down
CPL image estimation (KLT)
Difference map between CPL and original image
JND map
Drawbacks
Insufficient factors
Difficult to model their interaction
Merits
Bypassing complex and inaccurate modeling
Easy and efficient

## Slide 5
KLTJND: Top-Down JND model based on KLT
Motivation to apply KLT: theory of KLT
Input image
Patch vectorize
New matrix
Covariance matrix of
Eigenvalue decomposition
KLT kernel
Arrange eigenvector according to eigenvalue in descending order to obtain
KLT coefficient matrix , is the -th spectral component in .

## Slide 6
KLTJND: Top-Down JND model based on KLT
Motivation to apply KLT: image reconstruction
KLT kernel is an orthogonal matrix, thus , original image can be reconstructed as .
Take the first spectral components to obtain reconstruction KLT coefficient matrix as follows:
The image is reconstructed as by only considering the first spectral components. And here we adopt .

## Slide 7
KLTJND: Top-Down JND model based on KLT
Motivation to apply KLT: image reconstruction
When =16, the reconstructed image is perceptual lossless compared with the original one.

## Slide 8
KLTJND: Top-Down JND model based on KLT
Motivation to apply KLT: image reconstruction
When we take enough spectral components (first ) for image reconstruction, we will obtain the critical perceptual lossless (CPL) image. And is the critical point.

## Slide 9
KLTJND: Top-Down JND model based on KLT
JND estimation based on CPL image prediction
Convergence Property of KLT Coefficient Energy
KLT coefficient Energy for spectral component : .
The normalized KLT coefficient energy : .
The cumulative normalized KLT coefficient energy : , .
gradually converges which refers to reconstructed image becomes closer to the original one.

## Slide 10
KLTJND: Top-Down JND model based on KLT
JND estimation based on CPL image prediction
For images with different contents, although their cumulative distribution curves have the same convergence tendency, their critical points that lead to sufficient visual information may be different.
Convergence Property of KLT Coefficient Energy

## Slide 11
KLTJND: Top-Down JND model based on KLT
JND estimation based on CPL image prediction
Critical Point Derivation
500 images from DIV2K
Reconstructed image using the first spectral component,
participant Compare : no visible difference. Then critical point of original image given by participant . 60 users participate our experiment. Critical points of original image: . Then we adopt the criterion to exclude the outliers and will be updated to . The mean value of is . Then we set the final critical point for original image as .
Notes: DIV2K:
[1] R. Timofte et al., “NTIRE 2017 challenge on single image super-resolution: Methods and results,” in 2017 IEEE Conference on Computer Vision and Pattern Recognition Workshops (CVPRW), 2017, pp. 1110–1121.
[2] E. Agustsson and R. Timofte, “NTIRE 2017 challenge on single image super-resolution: Dataset and study,” in 2017 IEEE Conference on Computer Vision and Pattern Recognition Workshops (CVPRW), 2017, pp. 1122–1131.

## Slide 12
KLTJND: Top-Down JND model based on KLT
JND estimation based on CPL image prediction
Critical Point Derivation
We apply Shapiro-Wilk test to verify the normality of the votes distribution. 13 P-value < 0.05. The votes distributions of most images conform to normal distribution.
Notes: Shapiro-Wilk test:
[1] S. S. Shapiro and M. B. Wilk, “An analysis of variance test for normality (complete samples),” Biometrika, vol. 52, pp. 591– 611, 1965.

## Slide 13
KLTJND: Top-Down JND model based on KLT
JND estimation based on CPL image prediction
Critical Point Derivation
We compute for each original image and we obtain . It can be well approximated by Weibull distribution. Given an input image, as the critical point.

## Slide 14
KLTJND: Top-Down JND model based on KLT
JND estimation based on CPL image prediction
CPL Image Reconstruction
Then the image is reconstructed as , is the CPL image.
Use the first (critical point) spectral components for image reconstruction. The reconstruction KLT coefficient matrix is shown as follows:
JND Map Estimation
With the original image and CPL image , we could obtain the final JND map as follows:

## Slide 15
Experimental Results
Performance comparison on direct JND prediction
RMSE values between the predicted JND maps and the ground-truth JND map. KLTJND ranks 1st
Performance comparison on VLT dataset
Notes: VLT dataset:
[1] N. Ye, K. Wolski, and R. K. Mantiuk, “Predicting visible image differences under varying display brightness and viewing distance,” in 2019 IEEE/CVF Conference on Computer Vision and Pattern Recognition (CVPR), 2019, pp. 5429–5437.

## Slide 16
JND-guided noise injection
Noise injection with the guidance of the estimated JND map is shown as follows:
denotes the bipolar random noise of , and is a noise energy regulating factor to control the noise intensity which is measured by PSNR. Here we adopt HDR-VDP 2.2 and subjective study to compare the visual quality of noise injected images which are guided by different JND models.
Experimental Results
Notes: HDR-VDP 2.2:
[1] R. Mantiuk, K. J. Kim, A. G. Rempel, and W. Heidrich, “HDR VDP-2: a calibrated visual metric for visibility and quality predictions in all luminance conditions,” ACM Transactions on Graphics, vol. 30, no. 4, pp. 1–14, 2011.
[2] M. Narwaria, R. K. Mantiuk, M. Silva, and P. L. Callet, “HDR VDP-2.2: a calibrated method for objective quality prediction of high-dynamic range and standard images,” Journal of Electronic Imaging, vol. 24, no. 1, p. 010501, 2014.

## Slide 17
JND-guided noise injection
Images selected from DIV2K as the test images for performance comparison
Experimental Results

## Slide 18
JND-guided noise injection
Visual quality comparison for noise-injected images (PSNR=26dB). KLTJND ranks 1st
Experimental Results

## Slide 19
JND-guided noise injection
PSNR=26dB
Experimental Results

## Slide 20
JND-guided noise injection
Further more, we take HDR-VDP 2.2 as the indicator to predict the visual quality of noise injected image. Under different noise intensity, KLTJND always ranks 1st.
Experimental Results

## Slide 21
JND-guided noise injection
Performance comparison on maximum tolerable noise level measured by PSNR. KLTJND ranks 1st
Experimental Results

## Slide 22
JND-guided image compression
Bitrate: 0.0684 bpp
Bitrate: 0.0595 bpp
Bitrate: 0.0362 bpp
Before JPEG, we apply JND-guided preprocessor to smooth input image
Although the bitrate of Wu2017 is much lower, the visual quality of KLTJND is better.
Experimental Results
Notes: Wu2017:
[1] J. Wu, L. Li, W. Dong, G. Shi, W. Lin, and C.-C. J. Kuo, “Enhanced just noticeable difference model for images with pattern complexity,” IEEE Transactions on Image Processing, vol. 26, no. 6, pp. 2682–2693, 2017.

## Slide 23
JND-guided image compression
JND-guided preprocessor will reduce the bitrate and the visual quality as well. Thus we propose a new metric to indicate the performance of JND model
A higher value of means a better performance of JND model. Our proposed KLTJND still performs better.
Here QP=1 for JPEG.
Experimental Results

## Slide 24
JND-guided image compression
Adjust different QP value and KLTJND always performs better.
Experimental Results

## Slide 25
Conclusion
This paper has presented a novel top-down JND estimation model of natural images. It dedicates to estimating a CPL image first by exploiting the distribution characteristic of the cumulative normalized KLT coefficient energy and then calculating the difference map between the original image and CPL image as the JND map. The extensive experiments have demonstrate the superiority of our proposed model. The code are available at https://github.com/Zhentao-Liu/KLT-JND. For more detail, please refer to our paper.